## Slide 1: Tools and Supplies
Basic Maintenance and Light Repair
Notes: In order to complete any job within the automotive industry, you need to be aware of the tools and supplies that you will encounter and have to use. This presentation will list out those tools and supplies along with rules that apply to these tools.

## Slide 2: Basic tool rules
Notes: Some tools have specific rules that apply to them, but here are some rules that apply to all tools.

## Slide 3: Basic Tool Rules
Purchase quality tools
Keep tools organized
Keep tools clean
Use the right tool for the right job
Notes: Basic Tool Rules:
Purchase quality tools – the old saying goes, “you get what you pay for”, quality tools are lighter, stronger, easier to use and more dependable, they also have guarantees for free replacement in case they get messed up
Keep tools organized – technicians have hundreds of tool and they should be neatly arranged for quick access. Every tool should have its place so that they can be easily grabbed and not waste time or money
Keep tools clean – wipe the tools clean and dry after every use, if a tool is greasy or oily then it can be dangerous.
Use the right tool for the right job – a good technician knows when, where and why a particular tool will work better than another tool for a certain job.
While working in the lab, you need to keep in mind of these rules along with the general safety rules of the classroom.

## Slide 4: Tool storage
Notes: In order to comply with basic tool rule #2 – Keep tools organized, there needs to be a way that the tools can be organized and stored.

## Slide 5: Toolbox
Toolboxes are used to protect a technician’s tools
Three parts
  Large, lower roll around cabinet
  Upper tool chest that sits on the roll around cabinet
  A small carrying tray
Notes: The standard tool storage used by technicians is the toolbox.
A toolbox is designed to protect a technician’s tool and keep them all in one place.
A standard toolbox has three main parts:
large, lower roll around cabinet – holds bulky, heavy tools such as large power tools
Upper tool chest that sits on the roll around cabinet – holds commonly used tools so they are at eye level
A small carrying tray – holds frequently used tools that are carried to the job

## Slide 6: Tools
Notes: The following slides are a list of all tools that you need to know while working in the lab. You need to follow any rules and regulations that accompany these tools.

## Slide 7: Wrenches
Notes: The first tool we will learn about is the wrench

## Slide 8: Wrench Rules
Always select the right size wrench
Never hammer on a standard wrench to break loose a bolt or large nut
Pull on the wrench
Never use a steel bar or pipe to increase the length of a wrench for leverage.
Wrenches can use metric or standard measurements
Notes: Rules to follow when working with wrenches:
Always select the right size wrench. It must fit the bolt head snuggly. A loose fitting wrench will round off the bolt head.
Never hammer on a standard wrench to break loose a bolt or large nut. Slug wrenches are used for that.
Always try to pull on the wrench. This is so if the wrench slips, you are less likely to hurt your hand. When you must push on a wrench, use the palm of your hand and keep your fingers open
Never use a steel bar or pipe to increase the length of a wrench for leverage. This can not only be dangerous for you, but it can also cause bending or breaking of the wrench.
Wrenches can use either metric or standard measurement, although standard measurements (inches) is more common. The measurement is denoted on the handle of the wrench.

## Slide 9: Open-End Wrenches
Has an open jaw on both ends with each end a different size and set at a different angle
Should not be used on extremely tight nuts or bolts
  Weak jaws
Notes: We will now move into different types of wrenches.
The first we will talk about is the open-end wrenches.
These wrenches have open jaws on both end with each end being a different size and angled at two different angles.
The angles allow for the wrench to turn bolts and nuts with little swing space.
These wrenches should not be used on extremely tight nuts or bolts. They have weak jaws and the jaws will flex outward and round off the bolt head.

## Slide 10: Box-End Wrenches
Completely closed on both ends
Less likely to round off a bolt head
Two styles
  6-point opening
  12-point opening
Notes: Box-end wrenches have completely closed ends on both ends. This is to completely surround and grip the head of the nut or bolt.
These wrenches are less likely to round off a bolt head than an open-wrench
There are two styles that these wrenches come in: 6-point and 12-point opening.
The 6-point opening is the strong of the two and should be used on extremely tight, rusted, or partially rounded bolt or nut heads.

## Slide 11: Combination Wrenches
One end is box-end, the other is open-end
Both ends are the same size
Notes: A combination wrench has one end that is a box-end and the other is an open-end.
Both of the ends are the same size.
This is wrench provides the advantage of two types of wrenches for the price of one.

## Slide 12: Line Wrenches
A box-end wrench with a small opening or split in the jaw
Usually a 6-point box-end wrench
Notes: Line wrenches are box-end wrenches with a small opening or split in the jaw
The opening allows for the wrench to be slipped over fuel lines, brake lines, or power steering lines and onto the fitting nut.
Prevents damage to soft fittings.

## Slide 13: Ratcheting Wrenches
Contains a gear and lever mechanism within the box-end of the wrench
The other end contains an open-end
Notes: Ratcheting wrenches contain an open-end and a box-end.
The box-end contains a gear and lever mechanism so the wrench can be moved back and forth for rapid faster installation or removal.

## Slide 14: Socket Wrenches
Consists of a socket and a socket handle
Socket is a cylinder-shaped, box-end tool for removing or installing bolts and nuts
  One end fits over the handle (square end) and the other fits over the fastener.
  Sockets drive size
    The size of the square opening for the ratchet or tool handle
    Four drive sizes – ¼”, 3/8”, ½”, ¾” (most common being 3/8” and ½”)
      ¼” used on bolts and nut heads ¼” and smaller
      3/8” used on bolts and nut heads between ¼” and 5/8”
      ½” used on bolts and nut heads from 5/8” to 1”
      ¾” used on bolts and nut heads larger than 1”
  Point Types
    4-point, 6-point, 8-point, 12-point (most common being 6 and 12)
    6-points are required when a bolt is very tight an you don’t want to “round off” or strip the bolt head
Notes:       Consists of a socket and a socket handle
      Socket is a cylinder-shaped, box-end tool for removing or installing bolts and nuts
        One end fits over the handle (square end) and the other fits over the fastener.
        Sockets drive size
          The size of the square opening for the ratchet or tool handle
          Four drive sizes – ¼”, 3/8”, ½”, ¾” (most common being 3/8” and ½”)
            ¼” used on bolts and nut heads ¼” and smaller
            3/8” used on bolts and nut heads between ¼” and 5/8”
            ½” used on bolts and nut heads from 5/8” to 1”
            ¾” used on bolts and nut heads larger than 1”
        Point Types
          4-point, 6-point, 8-point, 12-point (most common being 6 and 12)
          6-points are required when a bolt is very tight an you don’t want to “round off” or strip the bolt head

## Slide 16: Socket Handles
Fit into the square opening of the socket
Handles have a gear and level mechanism so the wrench can be moved back and forth for rapid fastener installation or removal
Socket handles
  Standard ratchet
  Offset ratchet
  Stuffy ratchet
  Breaker bars
  Insulated breaker bars
Extensions are used between a socket and its handle o allow access to difficult-to-reach fasteners
Universal Joint
  A swivel that lets the socket wrench reach around obstructions
  It’s used between the socket and handle, with or without an extension
Notes:       Socket handles
        Fit into the square opening of the socket
        Handles have a gear and level mechanism so the wrench can be moved back and forth for rapid fastener installation or removal
        Socket handles
          Standard ratchet
          Offset ratchet
          Stuffy ratchet
          Breaker bars
            Is the strongest socket handle and provides the most leverage
            Should be used when breaking loose large or extremely tight bolts and nuts
          Insulated breaker bars
        Extensions are used between a socket and its handle o allow access to difficult-to-reach fasteners
        Universal Joint
          A swivel that lets the socket wrench reach around obstructions
          It’s used between the socket and handle, with or without an extension
          Avoid putting too much bend into the joint because it may bind and break

## Slide 17: Adjustable Wrenches
Adjustable jaws
Handy in case of emergencies
Notes: Adjustable wrenches have jaws that can be adjusted to fit different size bolts and nuts.
They should only be used when other types of wrenches will not fit.
These are handy to have in case of emergencies.

## Slide 18: Pipe Wrenches
Adjustable wrench used to grasp cylindrical objects
Has toothed jaws
Notes: Pipe wrenches are adjustable wrenches that are used to grasp cylindrical objects.
The toothed jaws dig into the object for better grip.
Since the jaws are teethed, never use it on parts that will be ruined by marks or nicks.

## Slide 19: Allen Wrenches
Hexagonal shaft-type wrench
Used to turn set screws on pulleys, gears and knobs
Notes: Allen wrenches are hexagonal shaft-type wrenches.
These are the wrenches that are given to you in the furniture assembly kits.
The wrenches are used to turn set screws on pulleys, gears, and knobs

## Slide 20: Additional Wrenches
Insulated ratcheting wrench
Reversing ratcheting wrench
Flex combination wrench
Half-moon, 12-point wrench
Chain wrench
Notes: Some additional wrenches that can be used:
Insulated ratcheting wrenches – used while doing work around high voltage parts
Reversing ratcheting wrenches
Flex combination wrenches
Half-moon, 12-point wrenches – works well for tight quarters
Chain wrenches – used to grasp oil filters for removal

## Slide 21: Screwdrivers
Notes: The next tool is screwdrivers.

## Slide 22: Screwdrivers
Used to remove or install screws
Select on that is wide enough to completely fill the screw slot
DO NOT hammer or pry objects using a screwdriver
Can be metric or standard
Notes: Next we will talk about screwdrivers.
Screwdrivers are used to remove or install screws.
When selecting a screwdriver, make sure that you pick one that is wide and thick enough to completely fill the screw slot.
If the screwdriver is too big or small it may damage not only the screwdriver, but it may also bore out the screw.
Do not hammer or pry objects using a screwdriver, unless you are using an impact driver
Screwdrivers can use the metric or standard measuring system. The standard system is more commonly used. The size of the screwdriver is denoted on the handle of the driver itself.

## Slide 23: Shapes
Standard
Phillips
Frearson
Torx
Clutch
Notes: There are five different shapes of screwdrivers that we are going to talk about
Standard
  A single blade that fits into the slot in the screw head
Phillips
  Two crossing blades that fit into a star-shaped screw slot
Frearson
  Similar to a Phillips head
Torx
  Used to remove and install Torx screws
    A Torx screw has a 6-point, star-shaped indentation formed into its head
  The shape of the indentation allows Torx screws to be rotate with a great deal of force, or torque, without damaging the head
Clutch
  Used for clutch-head fasteners which has a bow-tie shaped opening in its head

## Slide 24: Styles
Offset
Stubby
Starting Screwdriver
Notes: Other than the standard screwdriver, there are additional styles of screwdrivers that can have the various shapes.
Both offset and stubby screwdrivers are good to be used for loosening screws inside tight places such as a glove box.
A starting screwdriver holds the screw securely until the hole is started. Most of the time, these use magnetism to hold the screw in place.

## Slide 25: Scratch Awl
Looks like a screwdriver
Used to mark sheet metal
Notes: In addition to the standard shape and styles, there are other “screwdrivers” that we may see in the autoshop
A scratch awl is a tool that looks like a screwdriver
However, you do not use it like a screwdriver, you use it to mark sheet metal and place indentions into the metal

## Slide 26: Impact Driver
Used in junction with a hammer
Used to loosen extremely tight screws.
Notes: An impact driver is used in conjunction with a hammer to loosen extremely tight screws. When struck with a hammer, the river exerts powerful turning and downward forces to release the screw from the material.

## Slide 27: Pliers
Notes: Pliers

## Slide 28: Pliers
Used to grip, cut, crimp, hold and bend various parts
Don’t use pliers when another type of tool can work
Notes: Another set of tools that we will learn are pliers.
Pliers are used to grip, cut, crimp, hold and bend various parts.
If another tool can be used, then use that tool because pliers can also damage nuts, bolts, screws and additional parts.

## Slide 29: Slip-joint Pliers
Most common pliers used
Adjustable jaws
Notes: The most common type of pliers used are the slip-joint pliers.
These pliers have a slip-joint to allow for the jaws to be adjusted to grasp different size parts.

## Slide 30: Rib Joint Pliers
Similar to slip-joint pliers
They have a larger holding grip
Notes: Rib joint pliers are similar to slip-joint pliers but they open extra wide for holding very large objects.

## Slide 31: Needle Nose Pliers
Good for handling extremely small parts or reaching into highly restricted areas
Do not twist needle nose pliers
Notes: Needle nose pliers are excellent for handling extremely small parts or reaching into highly restricted areas.
Do not twist too hard on needle nose pliers, the long thin jaws of the pliers can be bent.

## Slide 32: Diagonal Cutting Pliers
Most commonly used cutting pliers
They are used to cut potter pins, wires and plastic ties.
Jaw shaped to cut flesh with the surface
Notes: Diagonal cutting pliers are also one of the most commonly used cutting pliers.
Their jaw shape allows for them to cut items flush with an adjacent surface.
They are mostly used to cut off cotter pins, wires and plastic ties.

## Slide 33: Vice Grip Pliers
Clamp and hold parts
Unscrew fasteners with stripped or rounded heads
Notes: Vice grip pliers are used to clamp onto and hold a part. This allows for the technicians to have both hands free to do other tasks.
They can be used to unscrew fasteners with stripped or rounded heads.
However, they should NEVER be used on undamaged nuts or bolts because the jaws can distort the surface.

## Slide 34: Snap Ring Pliers
Used to install snap rings
Equipped with pointed tips
Notes: Snap ring pliers have sharp, pointed tips for installing and removing special clips called snap rings.
Snap rings are used to hold onto a shaft externally to prevent the shaft from sliding out of position.

## Slide 35: Additional Pliers
Wire Stripping Pliers
Used to remove plastic insulation from wires
Battery Pliers
Jaws used for grasping corroded fasteners on battery cables
Notes: Two additional types of pliers that can be found are wire stripping pliers and battery pliers.
Wire stripping pliers are used to easily remove plastic insulation from different sized wires.
Battery pliers have jaws that are used for grasping corroded fasteners on battery cables.

## Slide 36: Hammers
Notes: Next is hammers

## Slide 37: Hammer Rules
Select the right size hammer
Always check that the hammer head is tight on the handle
Use a brass, plastic or dead blow hammer on parts and tools that can be damaged by a steel hammer
Grasp the hammer near the end of the handle and strike the part or tool squarely
Notes: Rules to follow when using hammers:
Select the right size hammer. If a large part is struck by a small hammer, then the hammer can fly backwards dangerously. If the hammer is too big, then the part can be damaged.
Always check that the hammer head is tight on the handle. If not, the head may fly off and cause injury or damage.
Use a brass, plastic, or dead blow hammer on parts and tools that can be damaged by a steel hammer. Use a steel hammer only when maximum driving force is required.
Grasp the hammer near the end of the handle and strike the part or tool squarely.

## Slide 38
Ball Peen Hammer
Most common type
One flat face and a round end
Made of steel
Sledgehammer
Very large, heavy head
Used to produce powerful blows
Notes: A ball peen hammer is the most common type of hammer.
It has one flat face for general striking and a round end for shaping metal parts such as sheet metal or rivet heads.
Ball peen hammers are made of steel.
Sledgehammers are very large, heavy steel hammers.
They are usually the heaviest hammer and are used to produce powerful blows.

## Slide 39
Brass Hammer
Has a soft head
Used on parts that need to not be scarred
Plastic Hammer
Light and soft head
Used when light blows are needed
Notes: A brass hammer has a soft, heavy head and is useful when scarring the surface of a part must be avoided.
The relatively soft head deforms to protect the part surface from damage.
A plastic hammer, or rawhide hammer has a slight and soft head.
It is used when light blows are needed to prevent parts breakage or damage to surfaces on small delicate parts.

## Slide 40
Rubber Mallet
Head made entirely of rubber
Is used on sheet metal or plastic parts such as garnish molding and wheel covers
Dead blow Hammer
Plastic coated, metal face that is filled with small metal balls called lead shots
Notes: A rubber mallet has a head made of solid rubber.
It will rebound or bounce upon striking and is not effective on solid metal parts.
It is recommended on many sheet metals or plastic parts, such as garnish molding and wheel covers.
Dead blow hammers are plastic coated, metal face and is filled with small metal balls called lead shots.
The extra weight of the lead shots prevents a rebound of the hammer when striking.
The plastic coating prevents surface damage.

## Slide 41: Chisels and punches

## Slide 42: The Difference?
Chisel
Used for cutting off damage or badly rusted nuts, bolts, and rivet heads
Punches
Used to make an indentation or hole in a surface
Notes: What is the difference between a chisel and punch?
A chisel is usually used for cutting off damage or badly rusted nuts, bolts, and rivet heads.
A punch is used to make an indention or hole in a surface.

## Slide 43: Types
Flat chisel
Cape chisel
Round-nose cap chisel
Diamond-point chisel
Chisel or punch holder
Center punch
Starting punch
Pin punch
Aligning punch
Notes: There are various types of both the chisel and the punch:
Flat chisel
Cape chisel
Round-nosed cap chisel
Diamond-point chisel
Chisel or punch holder
Center punch – used to mark parts for reassembly and to start a hole before drilling. The indentation will keep the drill bit from moving when first starting to drill
Starting punch – shank tapered all the way to the end, strong and can withstand moderate blows, used to drive pins, shafts and metal rods partway out of a hole.
Pin punch – a straight shank that is lighter than a starting punch, it is used after a staring punch to push a shaft or rod the rest of the way out of a hole.
Aligning punch – has a long, tapered shaft and is handy for lining up parts during assembly, it can be inserted into holes in mating parts and then wiggled to match up the holes, never use this punch as a center punch.

## Slide 44: Rules
Use the largest punch or chisel that will work
Keep both ends of a chisel or punch properly ground and shaped
When grinding a chisel or punch, grind slowly to avoid overheating the tool
Make sure to wear eye protection when using or grinding a chisel or punch
Notes: Some rules to follow when using a chisel or punch:
Use the largest punch or chisel that will work
Keep both ends of a chisel or punch properly ground and shaped. A chisel’s cutting edge should be sharp and square. A starting punch or a pin punch should be ground flat and square. A center punch should have a sharp point.
  After prolonged hammering, the top of a chisel or punch can become deformed and enlarged. This is called mushrooming. A mushroomed chisel or punch is dangerous so it needs to be ground off and formed into a chamfer
When grinding a chisel or punch, grind slowly to avoid overheating the tool. Excessive heat will cause the tool to turn blue, lose its temper and become soft.
Make sure to wear eye protection when using or grinding a chisel or punch

## Slide 45: files

## Slide 46: Files
Used to remove burrs, nicks and sharp edges
Classified by its length, shape and cutting surface
Coarse files should be used on soft materials
Fine files should be used on harder materials
Notes: Files are used to remove burrs, nicks and sharp edges. They are also used to perform other smoothing operations.
They are classified by length, shape and cutting surface.
Generally a coarse file with large cutting teeth should be used on soft materials such as plastic, brass, and aluminum.
Fine files with small cutting teeth are needed to produce a smooth surface and to cut harder materials, like cast iron or steel.

## Slide 47: Rules
Never use a file without a handle securely attached
To prevent undue file wear, apply pressure only on the forward stroke
  Lift the file on the backstroke
When filing, place one hand on the handle and the other on the file tip
Do not file too rapidly
  One file stroke per minute is fast enough
Never hammer or pry with a file
Make sure the file is clean
Notes: Rules to remember when using files:
Never use a file without a handle securely attached. If the file is used without a handle, the pointed tang can puncture your hand or wrist.
To prevent undue file wear, apply pressure only on the forward stroke. Lift the file on the backstroke.
When filing, place on hand on the handle and the other on the file tip. Hold the file firmly and do not press too hard.
Do not file too rapidly. One file stroke every second is fast enough. Count to yourself and time your strokes at 50-60 strokes per minute.
Never hammer or pry with a file. A file is very brittle and will break easily. Bits of the file can fly into your face or eyes.
If a file becomes clogged, clean it with a file card or a stiff wire brush.

## Slide 48: Types
Flat, single-cut
Flat, double-cut
Half-round
Three-corner
Round
Notes: There are five main types of files that we will see:
flat, single-cut
Flat, double-cut
Half-round
Three-corner
Round

## Slide 49: saws

## Slide 50: Hacksaw
Used to cut metal objects
Blades of various length can be mounted to the frame
When selecting a blade, at least two saw teeth should be in contact with the material at all times.
When cutting, place one hand on the hacksaw handle and the other on the end of the frame
  Press lightly and average 50-60 strokes per minute
Notes: Hacksaws are the primary saw used by an automotive technician.
      Used to cut metal objects
      Blades of various lengths can be mounted in the saw’s adjustable frame
      The blade teeth should point away from the handle and the blade should be fastened tightly in the frame.
      When selecting a blade, a rule of thumb to follow is at least two saw teeth should contact the material being cut at any given time.
        This prevents the teeth from catching on the material and potentially breaking.
      When cutting, place one hand on the hacksaw handle and the other on the end of the frame.
        Press down lightly on the forward stroke and release pressure on the backstroke
        Use 50-60 strokes per minute
        If cuts are made faster than this, the blade will quickly overheat, soften and become dull

## Slide 51: Holding tools

## Slide 52: Vise
Used to hold parts during cutting, drilling, hammering, and pressing
Is mounted on a workbench
Vise caps are used to prevent damage to a delicate part.
Notes: A Vise is the most common holding tool used for bigger projects.
Used to hold parts during cutting, drilling, hammering, and pressing operations
It is mounted on a workbench
Vise caps
Are used to prevent damage when mounting precision or delicate parts in a vise
Vise caps are soft metal jaw covers. They will not only protect the part but will provide a more secure grip

## Slide 53: Vise Rules
Never hammer on a vise to loosen or tighten it
Keep the moving parts of the vise oiled and clean
Wear safety googles when using a vise
Be careful to not damage the parts in the jaws
Use the vise caps when a precision part is held in the vise
Notes: Vise rules
1. Never hammer on a vise handle to tighten or loosen the vise. Use the weight of your body to turn the vise handle
2. Keep the moving parts of the vise clean and oiled
3. Wear safety glasses when using a vise. Tremendous clamping force can be exerted and parts may break and fly out
4. Be careful not to damage parts in the jaws of the vise
5. Use vise caps when a precision part is held in a vise. This will prevent part damage.

## Slide 54: C-clamp
Holds parts on a work surface
Various sizes for different projects
Notes: A portable holding tool is known as a C-Clamp.
These hold parts on a work surface when drilling, filing, cutting, welding or doing other operations.
There are various sizes depending on the scale of project that you are doing.

## Slide 55: Stands And Holding Fixtures
Used to secure heavy or clumsy parts during repairs
They make your work safer and easier
Notes: Stands and Holding Fixtures are used to secure heavy or clumsy parts during repair.
They make you work easier and safer when working with parts.
Some examples are a cylinder head stand, transmission fixture, and rear axle holding stand

## Slide 56: Cleaning tools
Notes: Cleaning tools are important due to their ability to remove carbon, rust, dirt, grease, old gaskets, and dried oil from parts.

## Slide 57: Scrapers
Remove grease, gaskets sludge, dried oil, and carbon on flat parts
Types
  Razor blade scrapers
  Gasket scrapers or putty knives
  Spring gasket scrapers
Notes: Scrapers are sharp tools that are used to remove grease, gaskets, sludge, dried oil, and carbon on flat parts.
Since these tools are so sharp, make sure to wear work gloves and keep your hands out of the way to avoid any serious injuries.
The three main types of scrapers that we will see in this unit are razor blade scrapers, gasket scrapers or putty knives, and spring gasket scrapers.

## Slide 58: Brushes
Used to remove light rust, paint and dirt on round or irregularly shaped parts
They are slow to use, so should only be used during certain times
Notes: Brushes are the other cleaning tool that you will see around the shop area.
They are used to remove light rust, paint and dirt on round or irregularly shaped parts in which a scraper can’t be used.
They are slow to use and should be used only when heavy, flaky, chalky deposits are coming off of the curved surface of the part.

## Slide 59: Probe and pickup tools
Notes: Probe and pickup tools are needed when bolts, nuts or other small parts are dropped and cannot be reach by hand.

## Slide 60: Magnetic Pickup Tool
Magnet hinged to the end of a rod
The rod can be shortened or lengthened
Can only be used on metal parts
Notes: The most common pickup tool used is the magnetic pickup tool.
The tool consists of a magnet hinged to the end of a rod.
The rod can be shortened or lengthened and can also swivel to reach into any area.
If a metal part is dropped, it will be attracted to and stick to the magnet on the end of the tool.

## Slide 61: Other Probe and Pickup Tools
Finger Pickup Tool
Used to grasp tools that are nonmagnetic
Consists of a small “claw” that is contracted by movements of your finger on a trigger
Mirror Probe
Allows you to look around corners or behind parts
Consists of a mirror angled on the end of a rod
Notes: Two additional tools that we may use include the finger pickup tool and the mirror probe.
The finger pickup tool is used to grasp tools that are nonmagnetic such as aluminum, plastic, and rubber.
It consists of a small claw on the end of a rod. The claw is contracted by movements of your finger on a trigger.
A mirror probe allows you to look around corners or behind parts for items that have dropped or leaks that may have occurred.
The mirror probe consists of a mirror angled on the end of a rod.

## Slide 62: Cutting tools

## Slide 63: Cutting Tools
Needed to open part boxes, cut off insulation, and do similar tasks
Razor blades are the most common
Notes: Cutting tools are important in the shop.
They are needed to open part boxes, cut off insulation, and do similar tasks.
Razor blades are the most common cutting tool but you can also see x acto knives.

## Slide 64: Pry bar

## Slide 65: Pry Bar
Strong steel bar
Helpful during assembly, disassembly and adjustment operations
Notes: A pry bar is just a simple steel bar.
It is very helpful during assembly, disassembly and adjustment operations in which parts need to be lifted, pried open or popped loose.
Since this bar is so strong, you need to be careful not to damage any part of the vehicle.

## Slide 66: Insulated tools
Notes: Insulated tools are designed to help protect against electric shock and electrocution when working on high-voltage circuits or 1000+ volts.
These are usually used for hybrid electric drive train service.

## Slide 67: Insulated Tools
Insulated wrench
Electrician’s pliers
Plastic pliers
Graphite screwdrivers
Notes: The main insulated tools that are used by the technician are:
Insulated wrench – conventional steel coated with synthetic plastic to prevent electric current from accidentally flowing through the wrench and your body
Electrician’s pliers – have a gripping and cutting surface for working with wiring but have insulated handles
Plastic pliers – made of solid insulating material for the highest protection when working with high-voltage hybrid electric drive train circuits.
Graphite screwdrivers – have a plastic handle and a plastic shank, while only the tip of the tool is made of conductive, hardened steel

## Slide 68: Compressed-air system
Notes: A compressed air-system is a necessity in all automotive shops.

## Slide 70: Air Compressor
Source of compressed air
Consists of an electric motor that spins an air pump which forces air into a large, metal storage tank
The compressor turns on and off automatically to maintain a preset pressure in the system
Notes: Air compressor
Source of compressed air
Normally has an electric motor that spins an air pump. The air pump forces air into a large, metal storage tank.
The air compressor turns on and off automatically to maintain a preset pressure in the system.

## Slide 71: Air Lines and Hoses
Metal airlines feed out from the air compressor’s tank
Flexible high pressure air hoses are connected to the metal lines
Quick-disconnect couplings are used to connect air hoses and air tools to the compressed air system without using a wrench
Notes: Air lines and Hoses
Metal airlines feed out from the air compressor’s tank
Flexible high-pressure air hoses are connected to the metal lines.
  These hoses allow the technician to take a source of air pressure to the vehicle being repaired
Quick-disconnect couplings are used to connect air hoses and air tools to the compressed air system without using a wrench.
  To join or separate a quick-disconnect coupling, pull back on the coupling’s outer sleeve with your finger pressure
  With the sleeve pulled back, you can push the coupling together or pull it apart.

## Slide 72: Pressure Regulator
Used to set a specific pressure in the compressed-air system
The shop pressure is usually set between 100 and 150 psi
Notes: Pressure regulator
Used to set a specific pressure in the compressed-air system
It’s called the shop pressure and is usually set between 100 and 150 pounds per square inch (psi)

## Slide 73
Filter
Removes water from the compressed system
Lubricator
Introduces oil into the airstream
Notes: The filter and the lubricator are both in place to increase the life of the air tools.
The filter removes water from the compressed system.
The lubricator introduces oil into the air stream

## Slide 74: Air tools
Notes: Air tools are powered by a compressed-air system

## Slide 75: Use
Always lubricate the tool before and after use
While pressing the air tool’s trigger, squirt a few drops of air tool oil into the tools air inlet fitting
This helps protect the internal parts of the tool
Hold a rag around the air outlet and run the oiled tool briefly to circulate the lubricant through the air motor
Excess oil will be sprayed into your shop rag
Wipe the tool clean before use or storage
Notes: There are a few steps that you need to follow when using any air tools
Always lubricate the tool before and after use
While pressing the air tool’s trigger, squirt a few drops of air tool oil into the tools air inlet fitting
This helps protect the internal parts of the tool
Hold a rag around the air outlet and run the oiled tool briefly to circulate the lubricant through the air motor
Excess oil will be sprayed into your shop rag
Wipe the tool clean before use or storage

## Slide 76: Impact Wrench
Heavy duty air wrenches
Use an air motor to produce a striking or hammering force that rotates the driving head
The driving head holds a special impact socket
Drive sizes
  ¼”, 3/8”, ½”, ¾”
A button or switch controls the direction of rotation
Notes: Impact wrench
Heavy-duty air wrenches that produce a great deal of torque to remove or install fasteners
They use an air motor to produce a striking, or hammering, force that rotates the driving head
The driving head holds a special impact socket
Drive Sizes
  ¼”
    Tiny machine screws in the interior or on trim pieces of the vehicle
  3/8”
    Ideal for small fasteners such as ¼” – 9/16” bolts
  ½”
    For general purpose use with medium to large fasteners such as ½” to 1” bolts and wheel lug nuts
  ¾”
    For extremely large fasteners found on trucks
A button or switch on the impact wrench controls the direction of rotation, usually clockwise to tighten and counterclockwise to loosen.

## Slide 77: Air Ratchet
Air wrench designed to quickly install or remove fasteners
Good for working in limited space
Doesn’t have high power, so most initial loosening and final tightening must be done with a hand tool
Drive size
  ¼”, 3/8”, ½”
Notes: Air ratchets
A special air wrench designed to quickly install or remove fasteners
Used for working in limited spaces but it does not have very much turning power
Final tightening and initial loosening most often has to be done with a hand tool
Drive sizes
  ¼”, 3/8”, ½”

## Slide 78: Impact Sockets And Extension
Must be used with air and electric wrenches
Are case-hardened steel that are thicker and stronger than conventional chrome-plated sockets
Notes: Impact sockets and extensions
Must be used with air and electric wrenches
Impact tools are case-hardened steel and are thicker and much stronger than conventional chrome-plated sockets and extensions
Have a flat black finish
These sockets, just like conventional sockets, can use either metric or standard measurements. The size of the socket is etched into the side of the socket.

## Slide 79: Air Hammer
Useful during various driving and cutting operations
Capable of producing about 1000-4000 impacts per minute
Notes: Air hammers are useful during various driving and cutting operations
They are capable of producing about 1000-4000 impacts per minute.

## Slide 80: Blowgun
Used to dry and clean parts
Used to blow dust and loose dirt off of parts
Always wear eye protection and direct the blast away from yourselves and others
DO NOT blow clean brake and clutch parts
Notes: Blowgun
Used to dry and clean parts washed in solvent
Used to blow dust and loose dirt from parts before or during disassembly
Always wear eye protection and direct the blast away from yourself and others
Do not blow clean brake and clutch parts because the dust from these parts contain asbestos

## Slide 81: Solvent Gun
Used to wash parts that will not fit into a cleaning tank
Notes: A solvent gun has the simple task of being used to wash parts that will not fit in the cleaning tank.

## Slide 82: Air Drill
Used for many tasks because of its power output and speed adjustment capabilities
With the use of attachments, air drills can drill holes, grind, polish and clean parts.
Notes: Air Drills
Used for many tasks because of its power output and speed adjustment capabilities
With the use of attachments, air drills can drill holes, grind, polish and clean parts.

## Slide 83: Air Brush Add-Ons
Rotary Brush
  Used for rapid cleaning of parts
Abrasive Pad
  Used for removal of old gasket material
Rotary File
  Used to removing metal burrs and nicks
Notes:       Rotary brush
        Used in an air drill for rapid cleaning of parts
        Can quickly remove old gasket material, carbon deposits, and rust with a minimum amount of effort
      Abrasive pad
        Cleaning tool used in an air drill
        Used for removing old gasket material
        Has the advantage of not scratching aluminum like a rotary brush can
      Rotary File
        Used in an air drill and is handy for removing metal burrs and nicks

## Slide 84: Electric tools

## Slide 85: Bench Grinder
Used for grinding, cleaning, or polishing operations
Two wheels
  Grinding wheel
  Wire wheel
Rules
  Always wear eye protection
  Have the shields in place
  Keep the tool rest adjusted close to the wheel
  Do not use a wire wheel to clean soft metal parts
Notes:       Used for grinding, cleaning or polishing operations
      Has two wheels
        Grinding wheel – used for sharpening and deburring metal tools, such as chisels and punches
        Wire wheel – used for cleaning and polishing metal tools, such as scrapers and putty knives
      Rules:
        Always wear eye protection and keep your hands away from the wheel
        Make sure the grinder shields are in place
        Keep the tool rest adjusted close to the wheel. If the rest is not close to the wheel, the part being ground can catch in the grinder.
        Do not use a wire wheel to clean soft metal parts, such as aluminum pistons or brass brushings. The abrasive action of the wheel can remove metal or scuff the part and ruin it. Instead use a solvent and a dull hand scraper on soft metal parts.

## Slide 86: Drills
Used to create holes in metal and plastic parts
Can be portable or mounted
Drill use bits that are shaped like the ends of screwdrivers
Bits can be metric or standard measurement
Notes:       Used to create holes in metal and plastic parts
      Can be portable or mounted.
      Bits
        Used in drills to drill holes in metal and plastic parts
        Mounted in the drill chuck
        A special key called a chuck key is sometimes needed to tighten the drill bit in the chuck
        Drill bits are commonly made of either carbon steel or high-speed steel
        Bits can me standard or metric measurement
        The measurement is either denoted on the bit itself, or on the holder for the bit.

## Slide 87: Portable Electric Drill
Hand-held drills
Wired and wireless
Electric drills with power cords are needed for more difficult or high-torque operations
Notes:       Portable electric drill
        Hand-held drills
        They come in different sizes
        Electric drills with power cords are needed for difficult or high-torque operations
          Commonly used sizes are ¼”, 3/8” and ½”

## Slide 88: Drill Press
Large, floor or bench mounted drill
The drill press allows the bit to be pressed into the work with increased force
Rules
  Remove the key from the chuck before turning on the drill press
  Secure the part to be drilled with a C-clamp
  Use a center punch to indent the part and start the hole
  Release the press right before the bit breaks through the bottom of the part
  Oil the bit as needed
Notes:       Drill press
        A large, floor- or bench-mounted drill needed for drilling large, deep or multiple holes in several parts
        The drill press allows the bit to be pressed into the work with increased force
        Larger drill bits can be used
        Drill press rules
          Remove the key from the chuck before turning on the drill press
          Secure the part to be drill with C-clamps or other holding fixtures
          Use a center punch to indent the part and start the hole
          To prevent injury, release drilling pressure right before the bit breaks through the bottom of the part. A drill bit tends to catch when breaking through. This can cause the drill or the part to rotate dangerously
          Oil the bit as needed. Oil pulls heat out of the bit and transfers it into the base metal being drilled. Without oil, a drill bit can overheat and lose its hardness before dulling quickly.

## Slide 89: Hydraulic tools

## Slide 90: Floor Jack
Used to raise either the front, sides or rear of a vehicle
Place the jack saddle under a solid part of the car, such as the frame, suspension arm, or axle housing.
To raise the vehicle, turn the jack handle or knob clockwise and pump the handle.
To lower the vehicle, turn the handle or knob counterclockwise slowly to open the pressure-release valve
When raising the vehicle, place the transmission in neutral and release the parking break
After raising, secure the vehicle on jack stands.
Notes:     Floor jack
      Used to raise either the front, sides or rear of a vehicle
      Place the jack saddle under a solid part of the car, such as the frame, suspension arm, or axle housing.
      To raise the vehicle, turn the jack handle or knob clockwise and pump the handle.
      To lower the vehicle, turn the handle or knob counterclockwise slowly to open the pressure-release valve
      When raising the vehicle, place the transmission in neutral and release the parking break
        This lets the vehicle roll, preventing it from pulling off of the jack
      After raising, secure the vehicle on jack stands.
        Place an automatic transmission in park and a manual transmission in gear.
        Apply the emergency brake and block the wheels

## Slide 91: Transmission Jack
Designed to hold transmissions and transaxles during removal or installation
Two types
  One to be used while the car is on the ground
  Other to be used while the car is raised on a lift
Notes:     Transmission jack
      Designed to hold transmissions and transaxles during removal or installation
      There are two types
        One is similar to a floor jack
        The other is taller and designed to be used while the vehicle is raised on a lift

## Slide 92: Engine Crane
Used to remove and install heavy engine assemblies
Equipped with a hydraulic hand jack for raising engines and a pressure-release valve for lowering engines
Can be handy for other heavy parts
Notes:     Engine crane
      Used to remove and install heavy engine assemblies
      Has a hydraulic hand jack for raising engines and a pressure-release valve for lowering engines
      Also handy for lifting intake manifolds, cylinder heads, engine blocks, transmissions, transaxles, and other heavy parts

## Slide 93: Hydraulic Press
Used to install or remove gears, pulleys, bearings, seals, and other parts requiring high pushing force
A hydraulic ram extends as the pump handle is worked
The ram presses the parts against a table
Notes:     Hydraulic press
      Used to install or remove gears, pulleys, bearings, seals and other parts requiring a high pushing force
      A hydraulic ram extends as the pump handle is worked.
      The ram presses the parts against a table

## Slide 94: Shop equipment

## Slide 95: Tire Changer
Used to remove and replace tires on wheels
Some are pneumatic and other are hand held
Notes:     Tire changer
      Used to remove and replace tires on wheels
      Some are pneumatic and other are hand held

## Slide 96: Jack Stands
Supports a vehicle during repairs
After raising the vehicle with a jack, place stack stands under the vehicle
Notes:     Jack stands
      Supports a vehicle during repairs
      After raising the vehicle with a jack, place stack stands under the vehicle

## Slide 97: Engine Stands
Used to hold an engine assembly once it is removed from the vehicle for rebuilding or repair
The engine cylinder block bolts to the stand just as it would to the transmission or transaxle
Notes:     Engine stands
      Used to hold an engine assembly once it is removed from the vehicle for rebuilding or repair
      The engine cylinder block bolts to the stand just as it would to the transmission or transaxle

## Slide 98: Cold-solvent Tank
Contains a pump, reservoir, and solvent and it is used to remove grease and oil from parts
After removing all old gaskets and scraping off excess grease, you can scrub the parts clean in the solvent.
A blowgun is then normally used to dry the solvent
Notes:     Cold-solvent tank
      Contains a pump, reservoir, and solvent and it is used to remove grease and oil from parts
      After removing all old gaskets and scraping off excess grease, you can scrub the parts clean in the solvent.
      A blowgun is then normally used to dry the solvent

## Slide 99: High-pressure Washer And Steam Cleaner
Can be used to remove heavy deposits of dirt, grease, and oil from the outside of large assemblies such as engine, transmissions and transaxles.
To keep the environment clean, wire brush the item to be cleaned and collect oil-soaked dirt before steaming or washing.
Notes:     High-pressure washer and steam cleaner
      Can be used to remove heavy deposits of dirt, grease, and oil from the outside of large assemblies such as engine, transmissions and transaxles.
      To keep the environment clean, wire brush the item to be cleaned and collet oil-soaked dirt before steaming or washing.

## Slide 100: Pressure Blaster
Used to clean rust or corroded parts.
Enclosed cabinet that has rubber gloves that extend into the cabinet for sandblasting and for cleaning dry parts.
Notes:     Pressure blaster
      Used to clean rust or corroded parts.
      Enclosed cabinet that has rubber gloves that extend into the cabinet for sandblasting and for cleaning dry parts.

## Slide 101: Oxyacetylene Torch
Used to heat, cut, weld or braze metal parts
Consists of an oxygen tank, an acetylene tank, pressure regulators, hoses and a hand-held torch
Service procedure
  Put on all necessary protective gear, including welding helmet or tinted goggles, thick leather welding gloves, and a leather jacket
  Inspect the oxyacetylene equipment for damage and make sure all cylinder, regulator, and torch valves are closes. Turn on the main gas valves on both tanks and check hoses for leaks
  Light the cutting torch according to the manufacturer’s recommendations
  With the torch held at a 90 angle to the work piece, concentrate the flame on the spot where the cut will begin.
  When the spot becomes cherry red, depress the oxygen-cutting lever to begin the cut
  Move the torch along the work piece slowly an steadily to make a continuous cut
  As soon as the cut is complete, release the cutting lever and shut off the torch and main tank valves
Notes:     Oxyacetylene torch
      Used to heat, cut, weld or braze metal parts
      Consists of an oxygen tank, an acetylene tank, pressure regulators, hoses and a hand-held torch
      Service procedure
        Put on all necessary protective gear, including welding helmet or tinted goggles, thick leather welding gloves, and a leather jacket
        Inspect the oxyacetylene equipment for damage and make sure all cylinder, regulator, and torch valves are closes. Turn on the main gas valves on both tanks and check hoses for leaks
        Light the cutting torch according to the manufacturer’s recommendations
        With the torch held at a 90 angle to the work piece, concentrate the flame on the spot where the cut will begin.
        When the spot becomes cherry red, depress the oxygen-cutting lever to begin the cut
        Move the torch along the work piece slowly an steadily to make a continuous cut
        As soon as the cut is complete, release the cutting lever and shut off the torch and main tank valves

## Slide 103: Welder
Uses a high electric current to create a high-powered electric arc to melt and fuse metal parts together
Notes:     Welder
      Uses a high electric current to create a high-powered electric arc to melt and fuse metal parts together

## Slide 104: Soldering Gun
Used to join wires during electrical repairs
An electric current heats the tip of the iron or gun
The hot tip is used to heat the wires
Solder is applied to the hot wires and it melts
Solder is a lead-tin alloy that hardens into a strong, solid connection
Notes:     Soldering gun
      Used to join wires during electrical repairs
      An electric current heats the tip of the iron or gun
      The hot tip is used to heat the wires
      Solder is applied to the hot wires and it melts
      Solder is a lead-tin alloy that hardens into a strong, solid connection

## Slide 105: Battery Charger
Used to re-energize a “dead” or discharged battery
It forces current back into the battery to recharge it
The red charger lead connects to the positive (+) battery terminal and the black charger lead connects to the negative (-) battery terminal.
Notes:     Battery charger
      Used to re-energize a “dead” or discharged battery
      It forces current back into the battery to recharge it
      The red charger lead connects to the positive (+) battery terminal and the black charger lead connects to the negative (-) battery terminal.

## Slide 106: Drop Light
Provides portable source of light
The light can be taken to the repair area under the vehicle or in the trunk, passenger compartment or engine compartment
They are accompanied by a hook so that they are able to be hung up for ease of use.
Notes:     Drop light
      Provides portable source of light
      The light can be taken to the repair area under the vehicle or in the trunk, passenger compartment or engine compartment
      They are accompanied by a hook so that they are able to be hung up for ease of use.

## Slide 107: Pullers
Used to remove seals, gears, pulleys, steering wheels, axles, and other pressed-on parts
Notes:     Pullers
      Used to remove seals, gears, pulleys, steering wheels, axles, and other pressed-on parts

## Slide 108: Creepers
Used when working under a car supported on jack stands.
It allows the technician to easily roll under vehicles without getting dirty
Stool Creeper
  Allows the technician to be at eye level with tires and brake systems.
Notes:     Creepers
      Used when working under a car supported on jack stands.
      It allows the technician to easily roll under vehicles without getting dirty
      Stool Creeper
        Allows the technician to be at eye level with tires and brake systems.

## Slide 109: Roll Around Cart
Used for taking a number of tools to the job
Notes:     Roll around cart
      Used for taking a number of tools to the job

## Slide 110: Covers
Fender covers
  Placed over the fenders, upper grille, or other body sections to prevent vehicle damage.
  They protect the paint or finish from nicks, scratches and grease
Seat covers
  Placed over seats to protect them from dirt, oil and grease that might be on your work clothes
Notes:     Covers
      Fender covers
        Placed over the fenders, upper grille, or other body sections to prevent vehicle damage.
        They protect the paint or finish from nicks, scratches and grease
      Seat covers
        Placed over seats to protect them from dirt, oil and grease that might be on your work clothes

## Slide 111: Computer
Used by some technicians to help with tasks including problem diagnosis, preprogramming of computer chips, bookkeeping and reference to service literature
Notes:     Computer
    Used by some technicians to help with tasks including problem diagnosis, preprogramming of computer chips, bookkeeping and reference to service literature

## Slide 112: Measuring Tools

## Slide 113: Rules
Never drop or overtighten a micrometer or caliper
Store micrometers, digital calipers, and other measuring tools where they cannot be damaged
Grasp the micrometer frame in your palm and turn the thimble with your thumb and finger
Hold the micrometer or caliper squarely with the work or false readings can result
Rock or swivel the micrometer as it is touched on round parts
Place a thin film of oil on the micrometer or caliper surfaces during storage
Always check the accuracy of a micrometer or caliper if it is dropped or struck, or after a long period of use
Notes: Some rules to follow when using measuring tools
1. Never drop or overtighten a micrometer or caliper. They are very delicate and their accuracy can be thrown off easily.
2. Store micrometers, digital calipers, and other measuring tools where they cannot be damaged. Keep them in wooden or plastic storage boxes
3. Grasp the micrometer frame in your palm and turn the thimble with your thumb and finger. The measuring faces should just drag on the part being measured.
4. Hold the micrometer or caliper squarely with the work or false readings can result. Closely watch how the spindle or jaws are contacting the part.
5. Rock or swivel the micrometer as it is touched on round parts. This will ensure the most accurate diameter measurement is obtained.
6. Place a thin film of oil on the micrometer or caliper surfaces during storage. This will keep the tool from rusting.
7. Always check the accuracy of a micrometer or caliper if it is dropped or struck, or after a long period of use. Standardized gauge blocks, available from you tool suppliers, are used for checking micrometer accuracy.

## Slide 114: Scale
Used to make low-precision linear measurements
It’s accurate to about 1/64” in most instances
Types
  Customary rule
  Pocket rule
  Metric rule
  Combination square
  Tape measure
  Yardstick
Notes: The first measuring tool is a scale
Used to make low-precision linear measurements.
It is accurate to about 1/64” in most instances
Types
  Customary rule
    Numbered lines that represent full inches
    The smaller, unnumbered lines, or graduations represent fractions of an inch, such as ½”, ¼”, 1/8” and 1/16”
  Pocket rule
    Typically 6” and is small enough to fit in your shirt pocket
  Metric rule
    Has lines representing millimeters
    Each numbered line equals 10 mm or 1 cm
  Combination square
    Sliding square that is mounted on a steel rule
    It is needed when the rule must be held perfectly square against the part being measured
  Tape measure
    Extends several feet or meters in length
    It is sometimes needed for large distance measurements during body, suspension, and exhaust system repairs
  Yardstick
    A rigid measuring device used for large lineal measurements up to one yard or one meter

## Slide 115: Caliper
Outside caliper
  Used to make external measurements
  Fitted over the outside of parts and adjusted so each tip touches the part
  Tips on the caliper are then held up to a ruler for measurement
Inside caliper
  Designed for internal measurements in holes and other openings
  Placed inside the hole and adjusted until the tips just touch the part
  Tips are then measured with a ruler
Vernier caliper
  A sliding measuring device that can make inside, outside, and depth measurements with 0.001” accuracy
  Its fast and easy to use
Notes: Calipers
Outside caliper
  Used to make external measurements when 1/64” accuracy is sufficient
  It is fitted over the outside of parts and adjusted so each tip just touches the part
  The caliper is the held up to a ruler and the distance between the tips is measured to determine the size of the part
Inside caliper
  Designed for internal measurements in holes and other openings
  It is placed inside the hole and adjusted until the tips just touch the part
  The caliper is the held up to a ruler and the distance between the tips is measured to determine the size of the part
Vernier caliper
  A sliding measuring device that can make inside, outside, and depth measurements with considerable accuracy
  Can take measurements as small as 0.001”
  Some have a dial gauge attached so that you can read the thousandths part of a measurement easier
  It is fast and easy to use, making it a useful tool for technicians to have

## Slide 117: Micrometer
Used to make very accurate measurements up to one-ten-thousandth of an inch
Outside micrometer
  Measuring external dimensions, diameters, or thickness
  Place it around the outside of the part
  Turn the thimble until both the spindle and anvil are lightly touching
  Read the graduations on the hub and thimble to determine the measurement
Inside micrometer
  Measuring internal measurements of holes, cylinders or other part openings
  Place it inside the opening
  Adjust the micrometer until it touches the walls of the opening
  Remove the micrometer and read the measurement
Depth micrometer
  Used for measuring the depth of an opening
  Position the base squarely on the part
  Turn the thimble until the spindle contacts the bottom of the opening
  Read the measurement
Notes: Micrometers
  Used to make very accurate measurements up to one-ten-thousandth of an inch (0.0001”) or one thousandth of a millimeter
  Outside micrometers
    Used for measuring external dimensions, diameters or thicknesses.
    Place it around the outside of the part
    Turn the thimble until both the spindle and anvil are lightly touching
    Finally, read the graduations on a the hub and thimble to determine the measurement
  Inside micrometers
    Used for internal measurements of large holes, cylinders, or other part openings
    Place the micrometer inside the opening
    Then, adjust the micrometer until it just touches the walls of the opening
    Finally, remove the micrometer and read the measurement
  Depth micrometers
    Helpful when precisely measuring the depth of an opening
    The base of the micrometer is positioned squarely on the part
    The thimble is turned until the spindle contacts the bottom of the opening.
    The depth micrometer is read in the same way as an outside micrometer, however the hub markings are reversed

## Slide 119: Reading a Micrometer
Customary Micrometer
Note the largest number visible on the micrometer sleeve (1 = 0.100”)
Count the number of graduation lines to the right of the sleeve
  Each full sleeve graduation equals 0.025”
Note the thimble graduation aligned with the horizontal sleeve line
  Each thimble graduation equals 0.001”
  Round off
Add the decimal values and any full inch to get the micrometer reading
Metric Micrometer
Similar to the customary except one revolution equals 0.500 mm
Read the largest visible number on the sleeve (1 = 1.00 mm)
Count the number of graduation lines (both above and below the horizontal sleeve) to the right of the sleeve
  Full sleeve equals 0.5 mm
Read the thimble graduation aligned with the horizontal sleeve
  Each thimble graduation equals 0.01 mm
Add the decimal values to get the micrometer reading
Notes: Reading a Customary Micrometer
  Note the largest number visible on the micrometer sleeve. Each number equals 0.100”
  Count the number of graduation lines to the right of the sleeve number. Each full sleeve graduation equals 0.025”
  Note the thimble graduation aligned with the horizontal sleeve line. Each thimble graduation equals 0.001”. round off when the sleeve line is not directly aligned with a thimble graduation
  Add the decimal values from steps 1, 2,and 3. Add any full inches. This sum is the micrometer reading in inches.
Reading a Metric Micrometer
  Similar to a customary micrometers but one revolution of the thimble equals 0.500 mm.
  Read the largest visible on the micrometer sleeve. Each number equals 1.00 mm
  Count the number of graduation lines (both above and below the horizontal sleeve line) to the right of the sleeve number. Each full sleeve graduation equal 0.5 mm
  Read the thimble graduation aligned with the horizontal sleeve line. Each thimble graduation equals 0.01 mm
  Add the values from the steps 1, 2, and 3. This sum is the metric micrometer

## Slide 120: Feeler Gauge
Used to measure small clearances or gaps between parts
Flat feeler gauge
  Precision-ground steel blades of various thickness
  Used to measure distance between parallel surfaces
Wire feeler gauge
  Precise-size wires labeled by diameter or thickness
  Used to measure slightly larger spaces or gaps than a flat feeler gauge
  Used for measuring the distance between unparalleled or curved surfaces
How to use a feeler gauge
  Find the gauge blade or wire that just fits between the two parts being measured
  the gauge should be dragged slightly when pulled between the two surfaces
  The size on the gauge is the clearance between the two components
Notes: Feeler gauges
  Used to measure small clearances or gaps between parts.
  Flat feeler gauges have precision-ground steel blades of various thickness
    Thickness is written on each blade in thousandths of an inch and/or in hundredths of a millimeter.
    A flat feeler gauge is normally used to measure distance between parallel surfaces
  Wire feeler gauge has precise-size wires labeled by diameter or thickness.
    It is normally used to measure slightly larger spaces or gaps than a flat feeler gauge
    Also used for measuring the distance between unparalleled or curved surfaces
  How to use a feeler gauge
    Find the gauge blade or wire that just fits between the two parts being measured
    The gauge should be dragged slightly when pulled between the two surfaces
    The size given on the gauge is the clearance between the two components

## Slide 122: Dial Indicator
Used to measure part movement in thousandths of an inch
The needle or digital display on the indicator face registers the amount of plunger movement
Used to check gear teeth backlash, shaft end play, cam lobe lift and similar kinds of part movements
Using a dial indicator
  Mount the indicator securely and position the dial plunger parallel with the movement to be measured
  Partially compress the indicator plunger before locking the indicator into place.
  Move the part back and forth or rotate the part while reading the indicator
  Subtract the lowest reading from the highest reading
  The result equals the distance the part moved, the clearance, or the run out
Notes: Dial indicator
  Used to measure part movement in thousandths of an inch
  The needle or digital display on the indicator face registers the amount of plunger movement
  Frequently used to check gear teeth backlash, shaft end play, cam lobe lift, and similar kinds of part movements
  Using a dial indicator
    Mount the indicator securely and position the dial plunger parallel with the movement to be measured
    Partially compress the indicator plunger before locking the indicator into place. This allows part movement in either direction to be measured
    Move the part back and forth or rotate the part while reading the indicator
    Subtract the lowest reading from the highest reading. The result equals the distance the part moved, the clearance, or the run out.

## Slide 124: Temperature Measurement
Also known as thermometers
Used to measure temperature
The temperature obtained with the gauge can be compared to specifications
Notes: Temperature measurement
  Thermometers
  Used to measure temperature
  For example, air conditioning output temperature or radiator temperature may need to be determined
  The temperature obtained with the gauge can be compared to specifications

## Slide 125: Torque Wrench
Not used for measuring but is used to apply a specific amount of pressure or turning force to a fastener
Pressure is measured in foot-pounds or Newton-meters
Notes: Torque wrench
  Not used for taking measurements, rather its used to apply a specific amount of turning force to a fastener, such as a bolt or nut
  Torque wrench scales usually read in foot-pounds and Newton-meters

## Slide 126: Pressure Gauge
Used to measure air or fluid pressure in various systems and components
Usually reads in pounds per square inch, kilograms per square centimeter or kilopascals
Notes: Pressure gauge
  Used to measure air or fluid pressure in various systems and components
  Used to check tire air pressure, fuel pump pressure, air conditioning system pressure, or engine compression stroke pressure
  A pressure gauge normally reads in pounds per square inch, kilograms per square centimeter, or kilopascals

## Slide 127: Vacuum Gauge
Measures negative pressure or vacuum
Reads in inches of mercury or metric kilograms per square centimeter
Notes: Vacuum gauge
  Measure negative pressure or vacuum
  Similar to a pressure gauge reads in inches of mercury or metric kilograms per square centimeter
  For example, a vacuum gauge is used to measure the vacuum in an engine’s intake manifold

## Slide 128: Telescoping Gauge
Measures internal part bores or openings
To use the gauge
  Compress the spring-loaded extensions and lock them with the thumb wheel
  Insert the gauge into the opening and release the thumb wheel
  The extensions snap to the edges of the opening
  Use the thumb wheel to lock the extensions to the size
  Finally use an outside micrometer to measure the distance across the extensions
Notes: Telescoping gauge
  Used to measure internal part bores or openings.
  To use the gauge, compress the spring-loaded extensions and lock them with the thumb wheel
  Then insert the gauge into the opening and release the thumb wheel
  The extensions snap to the edges of the opening
  Use the thumb wheel to lock the extensions to the size
  Finally use an outside micrometer to measure the distance across the extensions

## Slide 129: Hole Gauge
Used for measuring very small holes in parts
To use the gauge:
  Loosen the thumb wheel
  Insert the gauge into the hole and tighten the thumb wheel until the gauge just touches the part
  Finally remove the gauge and measure it with an outside micrometer
Notes: Hole gauge
  Used for measuring very small holes in parts.
  To use a hole gauge, first loosen the thumb wheel.
  Then, insert the gauge into the hole and tighten the thumb wheel until the gauge just touches the part.
  Finally, remove the gauge and measure it with an outside micrometer